High Performance Python : Beyond Numpy
Jérôme Kieffer
Online Data Analysis

---
Layout
1. No optimization without profiling
2. Cython: Python binary modules in Python
3. PyOpenCL: GPU programming

---
Only optimize profiled code !
- Use the profiler from python:
  python -m cprofile -o log my_prog.py
- Visualization :
  - Using pstats module
  - Or better : visualize with runsnake
- Or simply use timeit (with ipython)

---
Exercise 0: Profile the code
- Check if a point is inside a polygon :
  - Code is in 0_Python
  - Profile the code considering :
    - 24-edges polygon
    - 1024x1024 pixels in image to check
Execution time on a bi-Xeon5520 (2.27GHz):
Based on tuples: 37s
Based on numpy: 157s

---
Visualization with runsnake

---
1. Cython
- Python binary extension written in Python
  - Translates python code to C/C++
  - Provides speed but needs compilation
  - Built-in support of numpy arrays
  - Can interface with C/C++ libraries (wrapping)
- Cython is getting mainstream for many projects:
  - Lxml, pyzmq, h5py, scikit image and learn,

---
Extension to python
- Cython modules have .pyx extensions
  - Just copy your python file with another extension
  - Convert your code to C using cython -a prog.pyx
  - option -a produces a webpage with annotation

---
Building a Cython module
- Using a setup.py is recommended:
  #!/usr/bin/python
  from distutils.core import setup
  from Cython.Distutils import build_ext
  from distutils.extension import Extension
  cy_mod=Extension("inside_polygon",
  sources=	["inside_polygon.pyx"])
  setup(ext_modules = [cy_mod],
  cmdclass = {'build_ext': build_ext})
- Build module using:
  $ python setup.py build_ext -i

---
Exercise: Compile a binary module
Speed-up: 4x just by compiling !

---
Cython optimization
- Benchmark your code
- inspect the annotated page (option -a)
  - Remove the yellow in the critical part
- Use cdef to enforce the type of variables
  - Will prevent the type checking which slows down Python

---
Annotated file
The lighter, the better / faster
Click on a line to see the generated code

---
Python or Cython classes

---
Wrapping C library
- C libraries can declared:
  cdef extern from "InsidePolygonWithBounds.h":
    void PointsInsidePolygon(double *, int , \
            double *, int , int ,\	unsigned char *) nogil
- Cython offers a set of cimport libraries:
  - from libc.stdlib cimport malloc, free
  - from libc.string cimport memset, memcpy
- Include files can be merged into a .pxd
  from InsidePolygon cimport PointsInsidePolygon

---
Exercise: Compile a binary module
Speed-up: 4x just by compiling !

---
Exercise: use a cython class

---
Wrap C++ library
Directly inline:

---
Use an external include and pxd

---
Use OpenMP to parallelize
With nogil

---
Summary of speed-ups
	Execution time	Speed-up
Python with tuples	36 s	1
Python with numpy	157s	0.23
Cython with tuples	9 s	4
Cython with numpy+Opt	3.6	10
Cython_class + Opt	0.46	80
Cython with OpenMP	0.11	327
Measured on a dual-quadcore @2.27 GHz Xeon 5520

---
2. OpenCL
- An overview of OpenCL
- Programming GPU using PyOpenCL
Next slides come from:
https://github.com/HandsOnOpenCL/Lecture-Slides/releases

---
It’s a Heterogeneous world
A modern computing platform includes:
- One or more CPUs
- One of more GPUs
- DSP processors
- Accelerators
- … other?
E.g. Samsung® Exynos 5:
Dual core ARM A15 1.7GHz, Mali T604 GPU
E.g. Intel XXX with IRIS
OpenCL lets Programmers write a single portable program that uses ALL resources in the heterogeneous platform

---
Microprocessor trends
Individual processors have many (possibly heterogeneous) cores.
10 cores
16 wide SIMD
61 cores
16 wide SIMD
16 cores
32 wide SIMD
ATI™ RV770
Intel® Xeon Phi™ coprocessor
NVIDIA® Tesla® C2090
The Heterogeneous many-core challenge:
    How are we to build a software ecosystem for the
   Heterogeneous many core platform?
Third party names are the property of their owners.

---
Industry Standards for Programming Heterogeneous Platforms
GPUs
Increasingly general purpose data-parallel computing
CPUs
Multiple cores driving performance increases
Emerging
Intersection
Graphics APIs and Shading Languages
Multi-processor programming – e.g. OpenMP
Heterogeneous
Computing
OpenCL – Open Computing Language
Open, royalty-free standard for portable, parallel programming of heterogeneous parallel computing CPUs, GPUs, and other processors

---
The origins of OpenCL
ARM
AMD
Nokia
Merged, needed commonality across products
IBM
ATI
Sony
Qualcomm
Wrote a rough draft straw man API
Imagination
GPU vendor – wants to steal market share from CPU
TI
NVIDIA
+ many more
Khronos Compute group formed
CPU vendor – wants to steal market share from GPU
Intel
Was tired of recoding for many core, GPUs.
Pushed vendors to standardize.
Apple
Third party names are the property of their owners.

---
OpenCL Working Group within Khronos
Diverse industry participation
  - Processor vendors, system OEMs, middleware vendors, application developers.
- OpenCL became an important standard upon release by virtue of the market coverage of the companies behind it.
Third party names are the property of their owners.

---
OpenCL Timeline
- Launched Jun’08 … 6 months from “strawman” to OpenCL 1.0
- Rapid innovation to match pace of hardware innovation
  - 18 months from 1.0 to 1.1 and from 1.1 to 1.2
  - Goal: a new OpenCL every 18-24 months
  - Committed to backwards compatibility to protect software investments
During 2H09
Multiple conformant implementations ship across a diverse range of platforms.
Nov11
Jun10
Dec08
Release of OpenCL 1.2
Khronos publicly releases OpenCL 1.1 specification. Conformant implementations available shortly thereafter
Khronos publicly releases OpenCL 1.0 specification

---
OpenCL: From cell phone to supercomputer
OpenCL Embedded profile for mobile and embedded silicon
  - Relaxes some data type and precision requirements
  - Avoids the need for a separate “ES” specification
- Khronos APIs provide computing support for imaging & graphics
  - Enabling advanced applications in, e.g., Augmented Reality
- OpenCL will enable parallel computing in new markets
  - Mobile phones, cars, avionics
A camera phone with GPS processes images to recognize buildings and landmarks and provides relevant data from internet

---
OpenCL Platform Model
One Host and one or more OpenCL Devices
  - Each OpenCL Device is composed of one or more
    Compute Units
  - Each Compute Unit is divided into one or more Processing Elements
- Memory divided into host memory and device memory
Processing Element
OpenCL Device
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
Host
Compute Unit

---
OpenCL Platform Example
(One node, two CPU sockets, two GPUs)
CPUs:
GPUs:
Treated as one OpenCL device
  - One CU per core
  - 1 PE per CU, or if PEs mapped to SIMD lanes, n PEs per CU, where n matches the SIMD width
- Remember:
  - the CPU will also have to be its own host!
- Each GPU is a separate OpenCL device
- Can use CPU and all GPU devices concurrently through OpenCL
CU = Compute Unit; PE = Processing Element

---
Course materials
Course materials
In addition to these slides, C++ API header files, a set of exercises, and solutions, it is useful to have:
OpenCL 1.1 Reference Card
This card will help you keep track of the API as you do the exercises:
https://www.khronos.org/files/opencl-1-1-quick-reference-card.pdf
The v1.1 spec is also very readable and recommended to have on-hand:
https://www.khronos.org/registry/cl/specs/opencl-1.1.pdf

---
Lecture 3
Important OpenCL concepts

---
OpenCL Platform Model
One Host and one or more OpenCL Devices
  - Each OpenCL Device is composed of one or more
    Compute Units
  - Each Compute Unit is divided into one or more Processing Elements
- Memory divided into host memory and device memory
Processing Element
OpenCL Device
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
Host
Compute Unit

---
The BIG idea behind OpenCL
Replace loops with functions (a kernel) executing at each point in a problem domain
  - E.g., process a 1024x1024 image with one kernel invocation per pixel or 1024x1024=1,048,576 kernel executions
Traditional loops
Data Parallel OpenCL
void
mul(const int n,
    const float *a,
    const float *b,
        float *c)
{
  int i;
  for (i = 0; i < n; i++)
    c[i] = a[i] * b[i];
}
__kernel void
mul(__global const float *a,
    __global const float *b,
    __global float *c)
{
  int id = get_global_id(0);
  c[id] = a[id] * b[id];
}
// many instances of the kernel,
// called work-items, execute
// in parallel

---
An N-dimensional domain of work-items
Global Dimensions:
  - 1024x1024 (whole problem space)
- Local Dimensions:
  - 128x128 (work-group, executes together)
1024
Synchronization between work-items possible only within work-groups:
barriers and memory fences
Cannot synchronize between work-groups within a kernel
Choose the dimensions that are “best” for your algorithm
1024

---
OpenCL N Dimensional Range (NDRange)
The problem we want to compute should have some dimensionality;
  - For example, compute a kernel on all points in a cube
- When we execute the kernel we specify up to 3 dimensions
- We also specify the total problem size in each dimension – this is called the global size
- We associate each point in the iteration space with a work-item

---
OpenCL Memory model
Private Memory
  - Per work-item
- Local Memory
  - Shared within a
work-group
Global Memory /Constant Memory
  - Visible to all
work-groups
Host memory
  - On the CPU
Memory management is explicit:
You are responsible for moving data from
host → global → local and back

---
Context and Command-Queues
Context:
  - The environment within which kernels execute and in which synchronization and memory management is defined.
- The context includes:
  - One or more devices
  - Device memory
  - One or more command-queues
- All commands for a device (kernel execution, synchronization, and memory transfer operations) are submitted through a command-queue.
- Each command-queue points to a single device within a context.
Device
Device Memory
Queue
Context

---
Execution model (kernels)
OpenCL execution model … define a problem domain and execute an instance of a kernel for each point in the domain
__kernel void times_two(
    __global float* input,
    __global float* output)
{
   int i = get_global_id(0);
   output[i] = 2.0f * input[i];
}
get_global_id(0)
10
0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25
Input
Output
0	2	4	6	8	10	12	14	16	18	20	22	24	26	28	30	32	34	36	38	40	42	44	46	48	50

---
Building Program Objects
The program object encapsulates:
  - A context
  - The program kernel source or binary
  - List of target devices and build options
- The C API build process to create a program object:
  - clCreateProgramWithSource()
  - clCreateProgramWithBinary()
OpenCL uses runtime compilation … because in general you don’t know the details of the target device when you ship the program
GPU
code
__kernel void
horizontal_reflect(read_only image2d_t src,
        write_only image2d_t dst)
{
  int x = get_global_id(0); // x-coord
  int y = get_global_id(1); // y-coord
  int width = get_image_width(src);
  float4 src_val = read_imagef(src, sampler,
        (int2)(width-1-x, y));
  write_imagef(dst, (int2)(x, y), src_val);
}
CPU
code
Compile for GPU
Compile for CPU

---
Example: vector addition
The “hello world” program of data parallel programming is a program to add two vectors
C[i] = A[i] + B[i] for i=0 to N-1
For the OpenCL solution, there are two parts
  - Kernel code
  - Host code

---
Vector Addition - Kernel
__kernel void vadd(__global const float *a,
    __global const float *b,
    __global float *c)
 {
     int gid = get_global_id(0);
     c[gid] = a[gid] + b[gid];
 }

---
Vector Addition – Host
The host program is the code that runs on the host to:
  - Setup the environment for the OpenCL program
  - Create and manage kernels
- 5 simple steps in a basic host program:
  - Define the platform … platform = devices+context+queues
  - Create and Build the program (dynamic library for kernels)
  - Setup memory objects
  - Define the kernel (attach arguments to kernel functions)
  - Submit commands … transfer memory objects and execute kernels
As we go over the next set of slides, cross reference content on the slides to the reference card. This will help you get used to the reference card and how to pull information from the card and express it in code.

---
The basic platform and runtime APIs in OpenCL (using C)
CPU
GPU
Context
Programs
Kernels
Memory Objects
Command Queues
Programs
dp_mul
Buffers
Images
__kernel void
dp_mul(global const float *a,
       global const float *b,
       global float *c)
{
  int id = get_global_id(0);
  c[id] = a[id] * b[id];
}
arg [0] value
Out of
Order
Queue
dp_mul
CPU program binary
In
Order
Queue
arg [0] value
Out of
Order
Queue
In
Order
Queue
arg[0] value
arg [1] value
arg [1] value
arg[1] value
dp_mul
GPU program binary
arg [2] value
arg [2] value
arg[2] value
GPU
Compute Device

---
1. Define the platform
Use PyOpenCL to manage devices from Python
  import pyopencl
- In interactive mode one can immediately create a context:
  ctx = pyopencl.create_some_context()
Create a simple command-queue to feed our device:
queue = pyopencl.CommandQueue(ctx)
Inspect the device:
device = ctx.devices[0]
platform = device.platform
print(dir(device),dir(platform))

---
Command-Queues
Commands include:
  - Kernel executions
  - Memory object management
  - Synchronization
- The only way to submit commands to a device is through a command-queue.
- Each command-queue points to a single device within a context.
- Multiple command-queues can feed a single device.
  - Used to define independent streams of commands that don’t require synchronization
CPU
GPU
Queue
Queue
Context

---
Command-Queue execution details
Command queues can be configured in different ways to control how commands execute
In-order queues:
  - Commands are enqueued and complete in the order they appear in the program (program-order)
- Out-of-order queues:
  - Commands are enqueued in program-order but can execute (and hence complete) in any order.
- Execution of commands in the command-queue are guaranteed to be completed at synchronization points
  - Discussed later
Queue
Queue
Context
CPU
GPU

---
2. Create and Build the program
Define source code for the kernel-program as a string literal (great for toy programs) or read from a file (for real applications).
src = '''__kernel void vadd(__global const float *a,
    __global const float *b,
    __global float *c)
{
    int gid = get_global_id(0);
    c[gid] = a[gid] + b[gid]; }'''
Build the program object:
prg = pyopencl.Program(ctx, src)
Compile the program to create a “dynamic library” from which specific kernels can be pulled:
prg = prg.build()

---
Error messages
Fetch and print error messages:
if (err != CL_SUCCESS) {
 size_t len;
 char buffer[2048];
 clGetProgramBuildInfo(program, device_id,
  CL_PROGRAM_BUILD_LOG, sizeof(buffer), buffer, &len);
 printf(“%s\n”, buffer);
}
Important to do check all your OpenCL API error messages!
Easier in C++ with try/catch (see later)

---
3. Setup Memory Objects
- For vector addition we need 3 memory objects, one each for input vectors A and B, and one for the output vector C.
- Create input vectors and assign values on the host:
import numpy
h_a = numpy.random.random(LENGTH).astype(numpy.float32)
h_b = numpy.random.random(LENGTH).astype(numpy.float32)
h_c = numpy.empty((LENGTH,),dtype=numpy.float32)
Define OpenCL memory objects:
import pyopencl.array
d_a = pyopencl.array.to_device(queue , h_a)
d_b = pyopencl.array.to_device(queue , h_b)
d_c = pyopencl.array.empty(queue,(LENGTH,), dtype='float32')

---
What do we put in device memory?
Memory Objects:
A handle to a reference-counted region of global memory.
There are two kinds of memory object
- Buffer object:
  - Defines a linear collection of bytes (“just a C array”).
  - The contents of buffer objects are fully exposed within kernels and can be accessed using pointers
- Image object:
  - Defines a two- or three-dimensional region of memory.
  - Image data can only be accessed with read and write functions, i.e. these are opaque data structures. The read functions use a sampler.
Used when interfacing with a graphics API such as OpenGL. We won’t use image objects in this tutorial.

---
Creating and manipulating buffers
Buffers are declared on the host as type: cl_mem
Arrays in host memory hold your original host-side data:
float h_a[LENGTH], h_b[LENGTH];
Create the buffer (d_a), assign sizeof(float)*count bytes from “h_a” to the buffer and copy it into device memory:
cl_mem d_a = clCreateBuffer(context,
    CL_MEM_READ_ONLY | CL_MEM_COPY_HOST_PTR,
     sizeof(float)*count, h_a, NULL);

---
Conventions for naming buffers
It can get confusing about whether a host variable is just a regular C array or an OpenCL buffer
A useful convention is to prefix the names of your regular host C arrays with “h_” and your OpenCL buffers which will live on the device with “d_”

---
Creating and manipulating buffers
Buffers are declared on the host as type: cl_mem
Arrays in host memory hold your original host-side data:
float h_a[LENGTH], h_b[LENGTH];
Create the buffer (d_a), assign sizeof(float)*count bytes from “h_a” to the buffer and copy it into device memory:
cl_mem d_a = clCreateBuffer(context,
    CL_MEM_READ_ONLY | CL_MEM_COPY_HOST_PTR,
     sizeof(float)*count, h_a, NULL);

---
4. Define the kernel
Create kernel object from the kernel function “vadd”:
kernel = clCreateKernel(program, “vadd”, &err);
Attach arguments of the kernel function “vadd” to memory objects:
err = clSetKernelArg(kernel, 0, sizeof(cl_mem), &d_a);
err |= clSetKernelArg(kernel, 1, sizeof(cl_mem), &d_b);
err |= clSetKernelArg(kernel, 2, sizeof(cl_mem), &d_c);
err |= clSetKernelArg(kernel, 3, sizeof(unsigned int),	&count);

---
5. Enqueue commands
Write Buffers from host into global memory (as non-blocking operations):
err = clEnqueueWriteBuffer(commands, d_a, CL_FALSE,
        0, sizeof(float)*count, h_a, 0, NULL, NULL);
err = clEnqueueWriteBuffer(commands, d_b, CL_FALSE,
        0, sizeof(float)*count, h_b, 0, NULL, NULL);
Enqueue the kernel for execution (note: in-order so OK):
err = clEnqueueNDRangeKernel(commands, kernel, 1,
        NULL, &global, &local, 0, NULL, NULL);

---
5. Enqueue commands
Write Buffers from host into global memory (as non-blocking operations):
err = clEnqueueWriteBuffer(commands, d_a, CL_FALSE,
        0, sizeof(float)*count, h_a, 0, NULL, NULL);
err = clEnqueueWriteBuffer(commands, d_b, CL_FALSE,
        0, sizeof(float)*count, h_b, 0, NULL, NULL);
Enqueue the kernel for execution (note: in-order so OK):
err = clEnqueueNDRangeKernel(commands, kernel, 1,
        NULL, &global, &local, 0, NULL, NULL);

---
Exercise 2: Running the Vadd kernel
Exercise 2: Running the Vadd kernel
Goal:
  - To inspect and verify that you can run an OpenCL kernel
- Procedure:
  - Take the provided Vadd program. It will run a simple kernel to add two vectors together.
  - Look at the host code and identify the API calls in the host code. Compare them against the API descriptions on the OpenCL reference card.
  - There are some helper files which time the execution, output device information neatly and check errors.
- Expected output:
  - A message verifying that the vector addition completed successfully

---
N = 1024
# create context, queue and program
context = cl.create_some_context()
queue = cl.CommandQueue(context)
kernelsource = open(‘vadd.cl’).read()
program = cl.Program(context, kernelsource).build()
# create host arrays
h_a = numpy.random.rand(N).astype(float32)
h_b = numpy.random.rand(N).astype(float32)
h_c = numpy.empty(N).astype(float32)
# create device buffers
mf = cl.mem_flags
d_a = cl.Buffer(context, mf.READ_ONLY | mf.COPY_HOST_PTR, hostbuf=h_a)
d_b = cl.Buffer(context, mf.READ_ONLY | mf.COPY_HOST_PTR, hostbuf=h_b)
d_c = cl.Buffer(context, mf.WRITE_ONLY, h_c.nbytes)
# run kernel
vadd = program.vadd
vadd.set_scalar_arg_dtypes([None, None, None, numpy.uint32])
vadd(queue, h_a.shape, None, d_a, d_b, d_c, N)
# return results
cl.enqueue_copy(queue, h_c, d_c)
assert h_a+h_b == h_c